## Slide 1: “Don’t let the stack get stuck”: A novel approach for designing efficient stackable routers
Yoram Revah, Jose Yallouz,
Aviran Kadosh, Gideon Blocq, Ariel Orda
IEEE HPSR 2015
Marvell Israel and EE Technion

## Slide 2: Stackable Router
Cisco Catalyst 3750 Series Switches Topology
Stackable Routers - a class of standalone routers operating together to establish the characteristics of a single unit yet possessing the capacity of all devices.
Up to 9 switches
Connected in a Dual-Ring Topology
16 Gbps at each direction (total 32 Gbps)
24/48 100 Mbps ports (total 2.4/4.8 Gbps each switch)

## Slide 3: How to connect the Stackable Router?
Given 8 instances of a internal switches with 3 ports.
X8
How to connect them to minimize the diameter?
Notes: האם ניתן לחבר את הפיצה בוקס בצורה יותר יעילה מרינג?
מדד היעילות הדיאמטר.
לדוגמא: 8 פיצה בעלי 3 פורטים

## Slide 4: How to connect the Stackable Router?
Ring Topology
2
1
3
4
5
6
7
8
Notes: האם ניתן לחבר את הפיצה בוקס בצורה יותר יעילה מרינג?
מדד היעילות הדיאמטר.
לדוגמא: 8 פיצה בעלי 3 פורטים

## Slide 5: How to connect the Stackable Router?
Hypercube Topology
1
2
3
4
5
6
8
7
Notes: האם ניתן לחבר את הפיצה בוקס בצורה יותר יעילה מרינג?
מדד היעילות הדיאמטר.
לדוגמא: 8 פיצה בעלי 3 פורטים

## Slide 6: How to connect the Routers?
Octal Topology
Notes: האם ניתן לחבר את הפיצה בוקס בצורה יותר יעילה מרינג?
מדד היעילות הדיאמטר.
לדוגמא: 8 פיצה בעלי 3 פורטים

## Slide 7: Model Formulation
A stackable router is represented by a connected graph G(V,E)
  - the set of internal switches
  - the set of connections
Note

## Slide 8: Model Formulation

## Slide 9: Constructing the Stackable Router Topology
The PCODP problem is intractable!
Diameter Lower Bound:

## Slide 10: De-Bruijn Approach
000
001
100
010
101
011
110
111
Each node is labeled by a string of length under an alphabet of characters.
For example:
  Alphabet ().
  Length
Connect each string (c_1,...,c_m) with (c_2,...,x)) where x in the given alphabet

## Slide 11: De-Bruijn Approach
000
001
100
010
101
011
110
111
Each node is labeled by a string of length under an alphabet of characters.
For example:
  Alphabet ().
  Length
Undirected De Bruijn construction
  All self loop links are discarded.
  Transform all directed links into undirected

## Slide 12: De-Bruijn Approach
000
001
100
010
101
011
110
111
Diameter Approximation Factor:
does not depend on
Even for small
Notes: ביטוי השני בקושי משפיע על יחס.
עבור p קטן מקבלים יחס קרוב ל-1

## Slide 13: Simulation Results
We perform simulation on a random topology with different number of nodes and port quantity.
Port quantity

## Slide 14: Simulation Results
Comparison with the traditional ring topology.
Chart: Number of Nodes
| 50 | 100 | 150 | 200 | 300 | 400 | 800
p=3 | 3.453 | 5.7274 | 7.8288 | 9.8039 | 13.8249 | 17.8571 | 32.077
p=5 | 5.8275 | 9.9602 | 14.0713 | 16.7224 | 25 | 33.1126 | 57.1429
p=10 | 8.3333 | 14.4092 | 18.75 | 25 | 37.5 | 50 | 80

## Slide 15: Simulation Results
Approximation ratio of a random topology
Chart: Number of Nodes
| 50 | 100 | 150 | 200 | 300 | 400 | 800
p=3 | 1.7592 | 1.716 | 1.6917 | 1.6795 | 1.6307 | 1.585 | 1.5467
p=5 | 1.7418 | 1.697 | 1.6404 | 1.7304 | 1.6011 | 1.5273 | 1.5716
p=10 | 1.7845 | 1.7389 | 1.8352 | 1.7313 | 1.6034 | 1.5235 | 1.7002

## Slide 16: Agenda
Stackable Router Overview
Diameter Problem
Throughput Problem
Conclusion

## Slide 17: Throughput Problem Formulation
Notes: try to define the function
𝑓(𝐶) try to define the function

## Slide 18: Throughput Problem Formulation
Notes: try to define the function
𝑓(𝐶) try to define the function

## Slide 19: Conclusion
We investigated several design considerations in the construction of stackable routers.
Formalized an optimization problem for the diameter consideration (PCODP) :
  Lower bound for the optimal diameter
  De Bruijn approximation
  Simulations show that a random graph results in a close-to-optimal solution
Formalized an optimization problem for the throughput consideration (PCOTP) :
  Formalize the problem as an ILP
  Derive the integrality gap

## Slide 20
Thank you!